## Slide 1: Functional Safety Solutions for Automotive
FMEDA automation and predictable ISO 26262 compliance
Vladislav Palfy
vladislav.palfy@onespin.com

## Slide 2: IC Integrity
Functionally correct, safe, secure, and trusted SoCs/ASICs/FPGAs
Design
Integration
Implementation
IC Integrity
SoC/ASIC/FPGA Verification Flow
OneSpin provides certified IC Integrity Verification Solutions to develop functionally correct, safe, secure, and trusted integrated circuits.
Functional
Correctness
Safety
Trust and
Security

## Slide 3: IC Integrity
Functionally correct, safe, secure, and trusted SoCs/ASICs/FPGAs
Design
Integration
Implementation
IC Integrity
SoC/ASIC/FPGA Verification Flow
OneSpin provides certified IC Integrity Verification Solutions to develop functionally correct, safe, secure, and trusted integrated circuits.
Functional
Correctness
Safety
Trust and
Security

## Slide 4: Introduction to Functional Safety
The objective of functional safety:
Freedom from unacceptable risk of physical injury or of damage to the health of people either directly or indirectly
Risk management through functional safety standards
Risk drivers
Functional Safety Risks
Minimize systematic failures
Safeguard against random failures
Continuous increase in flow and tool complexity
Continuous increase in functionality
Increasing density of the design process node
Decreasing energy levels
Systematic Failures
  Design faults
  Tool faults
Random Failures
  Permanent faults
  Transient faults

## Slide 5: High-Level Safety Flow
Safeguard against random failures
Minimize systematic failures
Verification of the Safety Mechanism
HW Safety
Specification
Safety Mechanism Implementation
Functional Requirements Safety Requirements/Goals
Design Implementation
Functional Verification
Quantification of Verification
HW Specification
HW Safety Analysis
Diagnostic Coverage
Determination
Evaluation of
Hardware Metrics
Covered by OneSpin

## Slide 6: OneSpin FMEDA Methodology Overview
ISO 26262 compliant flow
HW Safety Analysis
Diagnostic Coverage
Determination
Evaluation of
Hardware Metrics
Safety Goals
ISO 26262 work products
in regards to random hardware failures

## Slide 7: Top Down and Bottom Up Safety Analysis
Safety Goal:
No unintended inflation of airbag, ASIL C/D
Failure Mode:
Wrong value from CPU
Failure:
4 + 4 = 4
Fault:
StuckAt 0 on bit reg[2]
Deductive
Top Down
Inductive
Bottom Up

## Slide 8: Hardware Safety Analysis
Failure Mode Contribution Analysis (FCA) App
Diagnostic Coverage
Determination
HW Safety Analysis
Evaluation of
Hardware Metrics
Safety Engineer analyzes
the failure modes causing
safety goal violations.
Hardware Design Safety Goals
But which failure mode can be caused by which fault?
Safety Goal
Failure Mode
Fault
And, which Safety Mechanisms are in place?
Notes: We ran this at over 2 billion transistors. Runs at SoC level. It’s a structural analysis.
Failure Mode is conversative

## Slide 9: Hardware Safety Analysis
Failure Mode Contribution Analysis (FCA) App
Diagnostic Coverage
Determination
HW Safety Analysis
Evaluation of
Hardware Metrics
Safety Engineer analyzes
the failure modes causing
safety goal violations.
The FCA App runs a structural HW safety analysis by linking failures to faults (failure mode distribution). This is a deductive (top down) analysis validated by an automated inductive coherency check.
Hardware Design Safety Goals
But which failure mode can be caused by which fault?
Safety Goal
Failure Mode
Fault
And, which Safety Mechanisms are in place?
Notes: We ran this at over 2 billion transistors. Runs at SoC level. It’s a structural analysis.
Failure Mode is conversative

## Slide 10: Hardware Safety Analysis
Failure Mode Contribution Analysis (FCA) App
Diagnostic Coverage
Determination
HW Safety Analysis
Evaluation of
Hardware Metrics
Safety Engineer analyzes
the failure modes causing
safety goal violations.
The FCA App runs a structural HW safety analysis by linking failures to faults (failure mode distribution). This is a deductive (top down) analysis validated by an automated inductive coherency check.
Hardware Design Safety Goals
Automated failure mode distribution reduces engineering effort.
Precise fault allocation minimizes/eliminates fault simulation.
But which failure mode can be caused by which fault?
Safety Goal
Failure Mode
Fault
And, which Safety Mechanisms are in place?
Notes: We ran this at over 2 billion transistors. Runs at SoC level. It’s a structural analysis.
Failure Mode is conversative

## Slide 11: FCA Example: FIFO with ECC Protection
FCA results with diagnostic coverage estimation
data
read
encode
decode
control
write
rd_data
rd_error
rd_corrected
full
empty
FFs
clk/rst
Sub part | Area / Failure Mode Distribution | State Count | Fault Count | Diagnostic Coverage
storage | 151.2 | 72 | 1024 | 100%
control | 32.3 | 8 | 434 | 0%
clk/rst-tree | 0.7 | 0 | 28 | 0%
active-encode | 4.4 | 0 | 52 | ?%
active-decode | 9.55 | 0 | 126 | ?%
passive-decode | 10.73 | 0 | 130 | ?%

## Slide 12: Hardware Safety Analysis Overview
ISO 26262 compliant flow
HW Safety Analysis
Diagnostic Coverage
Determination
Evaluation of
Hardware Metrics
Safety Goals
ISO 26262 work products
in regards to random hardware failures
Automated design analysis a key factor for efficient analysis of random hardware failures

## Slide 13: Diagnostic Coverage Determination
Fault Propagation and Detection Analysis (FPA/FDA) Apps
Diagnostic Coverage
Determination
HW Safety Analysis
Evaluation of
Hardware Metrics
How many faults are covered by safety mechanisms?
How many of the faults in the safety-related hardware element cannot violate the safety goal (Safe Fault Fraction)?
Hardware Design Safety Goals

## Slide 14: Diagnostic Coverage Determination
Fault Propagation and Detection Analysis (FPA/FDA) Apps
Diagnostic Coverage
Determination
HW Safety Analysis
Evaluation of
Hardware Metrics
How many faults are covered by safety mechanisms?
How many of the faults in the safety related hardware element cannot violate the safety goal (Safe Fault Fraction)?
Hardware Design Safety Goals
Expert judgment of diagnostic coverage leverages precise FCA fault allocation.
When expert judgment cannot be applied the FDA App determines the diagnostic coverage or fault simulation is applied.
FPA App automates safe fault extraction based on assumptions of use.

## Slide 15: Diagnostic Coverage Determination
Fault Propagation and Detection Analysis (FPA/FDA) Apps
Diagnostic Coverage
Determination
HW Safety Analysis
Evaluation of
Hardware Metrics
How many faults are covered by safety mechanisms?
How many of the faults in the safety related hardware element cannot violate the safety goal (Safe Fault Fraction)?
Hardware Design Safety Goals
Safe fault extraction eliminates manual fault analysis.
Automated diagnostic coverage determination does not require a testbench and can replace fault simulation.
Expert judgment of diagnostic coverage leverages precise FCA fault allocation.
When expert judgment cannot be applied the FDA App determines the diagnostic coverage or fault simulation is applied.
FPA App automates safe fault extraction based on assumptions of use.

## Slide 16: Fault Detection Analysis App Flow
Diagnostic coverage without simulation
Input
Constraints
Fault List
Observation
Points
Diagnostic
Points
FDA
Fault Classification
Report/DB
Fault
Inputs
RTL / Netlist
Detected (multipoint)
  Fault can propagate to at least one observation
  point and alarm is asserted
Non-detected (residual)
  Fault can propagate to at least one observation
  point and alarm is NOT asserted
Non-propagated (safe or latent)
  Fault does not propagate to observation
  points
encode
decode
control
FFs
Inject Faults in SMs

## Slide 17: FDA Example: FIFO with ECC Protection
Measuring diagnostic coverage for each sub-part
data
read
encode
decode
control
write
rd_data
rd_error
rd_corrected
full
empty
FFs
clk/rst
Sub part | Area / Failure Mode Distribution | State Count | Fault Count | Diagnostic Coverage
mem-data | 151.2 | 72 | 1024 | 100%
control | 32.3 | 8 | 434 | 0%
clk/rst-tree | 0.7 | 0 | 28 | 0%
active-encode | 4.4 | 0 | 52 | 100%
active-decode | 9.55 | 0 | 126 | 75%
passive-decode | 10.73 | 0 | 130 | 24%

## Slide 18: OneSpin FMEDA Methodology Overview
ISO 26262 compliant flow
HW Safety Analysis
Diagnostic Coverage
Determination
Evaluation of
Hardware Metrics
Safety Goals
ISO 26262 work products
in regards to random hardware failures
Automated design analysis a key factor for efficient analysis of random hardware failures

## Slide 19: Evaluation of Hardware Metrics
Hardware Metric Computation (HMC) App
Diagnostic Coverage
Determination
HW Safety Analysis
Evaluation of
Hardware Metrics
Which metrics must be produced to achieve ISO 26262 compliance?
Single-Point Fault Metric (SPFM)
    Reflects the robustness of the component with respect to safety goal violation by individual faults
Latent Fault Metric (LFM)
    Reflects the robustness of the component with respect to safety goal violation by multiple-point faults (faults in safety mechanism and function)
Probabilistic Metric for Random Hardware Failures (PMHF)
    Residual risk of the safety architecture. Measured by Failure in Time (FIT)
Hardware Design Safety Goals

## Slide 20: Evaluation of Hardware Metrics
Hardware Metric Computation (HMC) App
Diagnostic Coverage
Determination
HW Safety Analysis
Evaluation of
Hardware Metrics
Which metrics must be produced to achieve ISO 26262 compliance?
Single Point Fault Metric (SPFM)
    Reflects the robustness of the component with respect to safety goal violation by individual faults
Latent Fault Metric (LFM)
    Reflects the robustness of the component with respect to safety goal violation by multiple-point faults (faults in safety mechanism and function)
Probabilistic Metric for Random Hardware Failures (PMHF)
    Residual risk of the safety architecture. Measured by Failure in Time (FIT)
The HMC App enables full chip, multi-user, early estimation of the hardware metrics and compliance when data from FCA and the Diagnostic Coverage Determination becomes available.
Hardware Design Safety Goals

## Slide 21: Evaluation of Hardware Metrics
Hardware Metric Computation (HMC) App
Diagnostic Coverage
Determination
HW Safety Analysis
Evaluation of
Hardware Metrics
Which metrics must be produced to achieve ISO 26262 compliance?
Single Point Fault Metric (SPFM)
    Reflects the robustness of the component with respect to safety goal violation by individual faults
Latent Fault Metric (LFM)
    Reflects the robustness of the component with respect to safety goal violation by multiple-point faults (faults in safety mechanism and function)
Probabilistic Metric for Random Hardware Failures (PMHF)
    Residual risk of the safety architecture. Measured by Failure in Time (FIT)
The HMC App enables full chip, multi-user, early estimation of the hardware metrics and compliance when data from FCA and the Diagnostic Coverage Determination becomes available.
Hardware Design Safety Goals
No expert level ISO 26262 knowledge required and avoids spreadsheet madness.

## Slide 22: Hardware Metric Calculation Example
Web technology enables different use model
Calculates hardware metrics
SPFM
LFM
PMHF
Supports layering
Estimation layer
FCA layer
Client/Server architecture
Multi-user
Single DB

## Slide 23: OneSpin FMEDA Methodology Summary
ISO 26262 compliant flow
FMEDA
HW Safety Analysis
Diagnostic Coverage
Determination
Evaluation of
Hardware Metrics
Safety Goals
ISO 26262 work products
in regards to random hardware failures
Automated FMEDA flow for predictable ISO 26262 compliance
Reduce fault simulation
Reduce/eliminate manual analysis
Implement a repeatable, reusable and robust flow

## Slide 24
Thank You!